## Slide 1: Current and Potential Difference
STD 9 SCIENCE · CH. 3 CURRENT ELECTRICITY
Lesson 1 · Visual Science & Maths
Notes: Goal: students can define potential difference (V = W/Q) and current (I = Q/t), use volts, amperes and coulombs, and tell electron flow from conventional current.

## Slide 2: What makes a bulb light?
Flick a switch and the bulb lights at once, yet electrons only drift slowly through the wire.
What pushes them, and how do we measure their flow?
Teal dots: electrons. Coral arrows: conventional current
Notes: The whole wire is already full of free electrons; the cell pushes them all at once, like water in a full pipe.

## Slide 3: Electric charge
e = 1.6 × 10⁻¹⁹ C
Electrons carry negative charge
Unit of charge: coulomb (C)
1 C = charge of about 6.25 × 10¹⁸ electrons
Metals have free electrons that can move
Free electrons drifting round the circuit
Notes: Free electrons are the outermost electrons of metal atoms, only weakly held.

## Slide 4: Potential difference: the water analogy
A level difference keeps water flowing, like a cell keeps current flowing.
Equal levels: no flow. No potential difference: no current.
Notes: This mirrors the textbook activity with two bottles joined by a tube.

## Slide 5: Potential difference
V = W ÷ Q
Work done to carry unit positive charge between two points
Unit: volt (V) = 1 J/C
1 mV = 10⁻³ V, 1 kV = 10³ V
A cell keeps a potential difference between its terminals
Four cells: 6 V
Notes: Measure it with a voltmeter joined in parallel.

## Slide 6: Electric current
I = Q ÷ t
Charge passing per unit time
Unit: ampere (A) = 1 C/s
1 mA = 10⁻³ A, 1 µA = 10⁻⁶ A
Measured with an ammeter joined in series
Switch open: no complete path, no current
Notes: A current needs both a potential difference and a complete circuit.

## Slide 7: Which way does current flow?
− → +
Electrons
Drift from the negative terminal, round the circuit, to the positive terminal.
+ → −
Conventional current
Taken from positive to negative, opposite to the electrons.
Why?
History
The convention was fixed before electrons were discovered.
Notes: Circuit diagrams and rules always use conventional current.

## Slide 8: Worked examples
Charge from current
0.3 A flows through a torch bulb for 10 minutes. Find the charge.
t = 600 s
Q = 0.3 × 600 = 180 C
Potential difference
12 J of work moves 4 C between two points. Find the potential difference.
V = 12 ÷ 4 = 3 V
Notes: Always convert minutes to seconds first.

## Slide 9: Worked example: counting electrons
How many electrons make up 1 C? How many pass each second when the current is 2 A?
1 ÷ (1.6 × 10⁻¹⁹) = 6.25 × 10¹⁸
2 × 6.25 × 10¹⁸ = 1.25 × 10¹⁹ per second
1 A: 6.25 × 10¹⁸ electrons pass every second
Notes: Huge numbers of electrons move, each carrying a tiny charge.

## Slide 10: Common mistakes
Minutes in I = Q/t
Use seconds.
Current vs potential difference
Volts push; amperes flow.
Electrons go + to −
Electrons go − to +.
Ammeter across a bulb
Ammeter in series, voltmeter in parallel.
Notes: Meter connection errors are common in practical exams.

## Slide 11: Quick check
1
60 C passes through a wire in 2 minutes. Find the current.
2
Write 1 volt in terms of joules and coulombs.
3
Which way does conventional current flow outside a cell?
4
How is a voltmeter connected to measure the potential difference across a bulb?
Notes: Answers: 1) 0.5 A. 2) 1 V = 1 J/C. 3) From + to −. 4) In parallel, across the bulb.

## Slide 12: Count the charge yourself
Open the Current and Potential Difference lesson on the Visual Science & Maths website. Add cells, open the switch, and try the water analogy.
Next lesson: Resistance and Ohm's law
Notes: Homework idea: read the voltage printed on five batteries or chargers at home.