## Slide 1: Simple Machines
STD 9 SCIENCE · CH. 2 WORK AND ENERGY
Lesson 5 · Visual Science & Maths
Notes: This lesson follows the new NCERT Class 9 book. Goal: students can calculate mechanical advantage, use the law of the lever, classify levers and analyse a ramp.

## Slide 2: Lifting a rock with a bar
A 600 N rock is far too heavy to lift by hand. With a long crowbar, a 100 N push does it.
Where does the extra force come from?
Class I lever: effort arm 3 m, load arm 0.5 m
Notes: The machine does not create energy. The effort moves six times farther than the load.

## Slide 3: Mechanical advantage
MA = load ÷ effort
Effort: the force you apply
Load: the force you overcome
Work out is never more than work in
Less force means more distance
A ramp: 150 N over 6 m instead of 600 N over 1.5 m
Notes: Both give 900 J of work. The machine only changes how that work is delivered.

## Slide 4: The law of the lever
E × effort arm = L × load arm
Fulcrum: the fixed turning point
Arms are measured from the fulcrum
MA = effort arm ÷ load arm
A longer effort arm gives a bigger advantage
100 × 3 = 600 × 0.5
Notes: Try it with a ruler balanced on a pencil and coins as weights.

## Slide 5: Three classes of lever
I
Fulcrum in the middle
Seesaw, crowbar, scissors.
II
Load in the middle
Wheelbarrow, nutcracker, bottle opener. MA > 1.
III
Effort in the middle
Tongs, tweezers, forearm. MA < 1, but more speed.
Notes: Memory aid: the class number tells you what is in the middle: 1 fulcrum, 2 load, 3 effort.

## Slide 6: Class II and class III
Load 600 N, effort 200 N: MA 3.
Load 100 N, effort 400 N: MA 0.25.
A class III lever costs force but gains distance and speed at the load end.
Notes: Ask why we use tongs at all: precision and reach, not force.

## Slide 7: Ramps and pulleys
Ramp: MA = L ÷ h
Effort × L = load × h (no friction)
Longer, gentler ramp: less force needed
Fixed pulley: MA 1, changes direction
Movable pulley: ideal MA 2
L = 6 m, h = 1.5 m: MA = 4
Notes: A well pulley does not reduce the force; it lets you pull down using your body weight.

## Slide 8: Worked examples
A crowbar
Load 600 N, load arm 0.2 m, effort arm 1.2 m. Find the effort and MA.
E × 1.2 = 600 × 0.2, E = 100 N
MA = 600 ÷ 100 = 6
A loading ramp
An 800 N sack is pushed up a smooth 4 m ramp to a 1 m platform. Find the effort and MA.
E × 4 = 800 × 1, E = 200 N
MA = 4 ÷ 1 = 4
Notes: In both cases, work in = work out.

## Slide 9: Worked example: balancing a seesaw
A 20 kg child sits 1.5 m from the middle of a seesaw. Where must a 30 kg child sit to balance?
196 × 1.5 = 294 × d
d = 1 m from the middle
The heavier child sits closer to the fulcrum
Notes: g cancels, so 20 × 1.5 = 30 × d also works.

## Slide 10: Common mistakes
“Machines make energy”
They trade force for distance.
Arms from the bar's end
Measure from the fulcrum.
MA upside down
MA = load ÷ effort.
“Class III is useless”
It gives speed and reach.
Notes: Energy conservation from Lesson 3 explains why machines cannot give out more work than they take in.

## Slide 11: Quick check
1
A machine lifts 500 N with an effort of 125 N. Find its MA.
2
Which class of lever is a wheelbarrow?
3
What effort pushes a 400 N box up a smooth ramp 5 m long and 1 m high?
4
Can a simple machine reduce the work needed?
Notes: Answers: 1) 4. 2) Class II. 3) 80 N. 4) No; it can reduce the force, but the work stays the same or more.

## Slide 12: Balance a lever yourself
Open the Simple Machines lesson on the Visual Science & Maths website. Try all three lever classes and a ramp.
That completes Chapter 2: Work and Energy
Notes: Homework idea: find five levers at home and classify each one.