## Slide 1: Electricity at Home
STD 9 SCIENCE · CH. 3 CURRENT ELECTRICITY
Lesson 4 · Visual Physics
Notes: Goal: students can describe the three-wire system, explain why appliances are in parallel, calculate I = P/V, and explain fuses, MCBs and earthing.

## Slide 2: Behind the switch board
Every switch board hides three wires, a fuse and an arrangement that lets each appliance work on its own.
How does it all work, and how does it keep you safe?
Lights, fan and TV on a 15 A circuit
Notes: Start with what students can see at home: switches, sockets, the meter, the MCB box.

## Slide 3: Three wires
L
Live
Red or brown. Carries current at high potential (about 230 V).
N
Neutral
Black or blue. Completes the circuit back to the supply.
E
Earth
Green or yellow. Joined to a metal plate buried in the ground.
Notes: The supply in India is about 230 V (often quoted as 220 V).

## Slide 4: Appliances in parallel
I = P ÷ V
Each appliance is joined between live and neutral
Each gets the full 230 V
Each has its own switch
Currents add up in the main wires
215 W in total: 0.93 A
Notes: Switches always go in the live wire.

## Slide 5: The fuse at work
0.93 A: well below the 15 A rating.
19.6 A: the fuse melts and cuts the supply.
A fuse or MCB protects the wiring from overheating and fire.
Notes: An MCB is a switch that trips instead of melting, and can be reset.

## Slide 6: Why metal appliances are earthed
Fault current flows to earth, the fuse blows: safe.
Fuse does not blow; the iron's body is live: danger.
Notes: The earth wire carries current only when there is a fault.

## Slide 7: Worked examples
An electric iron
A 1000 W iron runs on 230 V. Find the current.
I = 1000 ÷ 230 ≈ 4.35 A
How many bulbs?
How many 100 W bulbs can run on a 5 A circuit at 230 V?
Max power = 230 × 5 = 1150 W
1150 ÷ 100 = 11.5, so 11 bulbs
Notes: Always round down when counting appliances against a fuse rating.

## Slide 8: Worked example: will the fuse blow?
A 15 A circuit supplies a 2000 W geyser, a 1500 W AC and a 1000 W iron together. Will the fuse blow?
Total power = 4500 W
I = 4500 ÷ 230 ≈ 19.6 A
19.6 A > 15 A: yes, it blows
4500 W on a 15 A circuit
Notes: Heavy appliances should be on separate, higher-rated circuits.

## Slide 9: Safety precautions
Out of reach
Keep switches and sockets away from small children.
Unplug first
Switch off and unplug before cleaning or repairs.
Dry hands
Never touch switches with wet hands; wear rubber soles.
Shock victim
Do not touch. Switch off or use a dry wooden stick.
Notes: Discuss each precaution and the physics behind it: water and bodies conduct; rubber and dry wood insulate.

## Slide 10: Common mistakes
Switch in neutral
Switches and fuses go in the live wire.
Higher fuse “for safety”
Use the correct rating or it will not protect.
Earth carries current normally
Only when there is a fault.
Touching a shock victim
Switch off the supply first.
Notes: These are life-safety points, not just exam points.

## Slide 11: Quick check
1
What colour is the earth wire's insulation?
2
How are household appliances connected?
3
A 2300 W geyser runs on 230 V. Find the current.
4
What does a fuse do when the current is too large?
Notes: Answers: 1) Green or yellow. 2) In parallel. 3) 10 A. 4) It melts and breaks the circuit.

## Slide 12: Wire a house yourself
Open the Electricity at Home lesson on the Visual Physics website. Switch on appliances, overload the fuse and test the earth wire.
That completes Chapter 3: Current Electricity
Notes: Homework idea: with an adult, find the MCB box at home and note the rating of each MCB.